## Slide 1: SMJE 3203 ARTIFICIAL INTELLIGENCE GROUP PROJECT FUZZY LOGIC BASED CONTROL SYSTEM FOR INTELLIGENT WASHING MACHINES GROUP 5 : CALVIN KANG ZHI TIAN A19MJ0019 OOI ZHENG MING A19MJ0224 HEE JIA MEI A19MJ0035 KHAW LI WEN A19MJ0040

## Slide 2: Introduction
Washing machines are common household appliances which has more effectively than traditional hand-wash approaches.
The users have been facing the problem of selecting the length of wash time based on the type of clothes, type of dirt, dirtiness of clothes and amount of clothes.
To overcome the problem, washing machines based on fuzzy logic offers the advantage of performance, simplicity and less cost.
A machine use of Fuzzy Logic mechanism to smartly calculate the amount of washing, rinsing, and spinning time in order to provide a precise real-time for the machine motor.

## Slide 3: Objective
To develop the fuzzy logic based intelligent washing machine system.
To implement the theoretical knowledge of fuzzy logic.
To design an intelligent washing machine which can save a lot of time, electricity, detergent and water for washing the clothes.

## Slide 4: Design for Fuzzy Logic Controller
Defuzzification
Centroid defuzzification
Fuzzification
Input parameters :
Type of clothes (TC)
Amount of clothes (AC)
Amount of dirtiness (AD)
Output parameters :
Wash time (Wash)
Rinse time (Rinse)
Spin time (Spin)
Inference Mechanism
Mamdani’s max-min inference method

## Slide 5: Rules

## Slide 6: Fuzzy Logic Modelling of Washing Machine
Crisp inputs → Fuzzy inputs (Membership function)
Type of clothes (TC) thin ,thick, and jeans, Amount of clothes (AC) little, normal, and large & Amount of dirtiness (AD) small, normal, and large
Rinse time very small, small, normal, long, and very long, Washing time small, normal and large & Spin time very small, small, normal, large and very large
Mamdani-style fuzzy inference process
Aggregation → Max, Implication → Min, MF→ Triangle & Symmetrical
Fuzzification of input variable. crisp values → fuzzy values. Fuzziness → the rules.
Control Rules in fuzzy design are set up
Aggregation of the rule outputs
Unification of the outputs of all rules which are extracted from membership functions
All rules are aggregated to combine them into a particular fuzzy set → to get a single fuzzy set
Input for defuzzification process.

## Slide 7: Fuzzy Logic Modelling of Washing Machine
4. Defuzzification (Centroid method)
Must be crisp number
Fuzzy set to a crisp set
Output: A single number is the controller’s response

## Slide 8: Expected result
Wash time might affected by the amount of dirtiness, type of clothes and amount of clothes.
Spin time might not affected much by the amount of dirtiness but type of clothes and amount of clothes affected has a much affected to it.
Rinse time might not affected much by the type of clothes but amount of dirtiness and amount of clothes affected has a much affected to it.

## Slide 9: Conclusion
Fuzzy logic is used for the washing machine response in differences conditions
The output of the washing machines affected by the input parameters. Example, more clothes might need more washing time.
The fuzzy logic is to help the the machine to finish it’s work with best result and more saving consumed power in differences conditions.

## Slide 10: Thank You